## Slide 1
ahutko@uw.edu 2021.03.22T17:00 UTC
Assessing SMA installs across & best practices

## Slide 2
TLDR
Quick n’ dirty overview of quality for each station:
https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS
Install a station less than 40m from not-only-slow traffic?

## Slide 3
Summary
-Less than 30m from traffic: keep lookin.
-Try to get at least 50m away from a road with traffic going faster than parking lot speeds, where traffic is more than 5 cars per hour during the day. Beyond ~70m cars won’t be why your station is a bad site. Less than 50m but near stop signs, roundabouts, tight spaces where cars only go very slow seem to be OK. <5 cars going by per hour at peak, e.g. certain 1 lane access roads, seem to be OK.
-Calm rivers aren’t that bad, though try to get away >50m from falling/white water. 3m from a small man made waterfall (UW.WWHS) = bad.
-Please take a “context” photo from far away that show the station in proximity to what you think might make noise: HVAC, generator, fridge, tower, solar panels, river... Also please add orientation, e.g your finger pointing North.
-An undergrad should go through all IRIS/SIS Lat/Lon and confirm with photos in nextcloud; usually if those are wrong, shop files are different and correct.
-Try to get away from “sails” (towers, solar panels) and decouple outdoor stations as much as possible from big structures. Low foot traffic indoor can be OK, big HVAC units within a few feet can be an issue, small heaters seem to be OK.
-Dams and power substations that are >50m from trafficy roads are all very good stations. UO.WALD at 13m from road is the bad one; even UO.LAKE at 34m from road is only “approaching worrisome”.

## Slide 4
Station reports
https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS
Noise floor:
“can I detect small nearby quakes?”
(not a priority for 3ch sites, but nice to have)
% of time above BAD - - - - - line

## Slide 5
Station reports
https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS
How many big bumps each hour
How many small bumps each hour
Hourly “damn, I can feel that” bumps
% of time above BAD - - - - - line
cares about these

## Slide 6
vs
Apples to apples normal vs covid shutdown comparison

## Slide 7
vs
Small bumps
Big bumps

## Slide 8
2 week average is not fair… Look at 80th percentile or 10am – 2pm
For coordinators group:

## Slide 9
Measured over 2-4 weeks, pre-covid if possible. 75th percentile highest values are plotted (captures “what does it look like during business hours”)
>140m

## Slide 10
>140m
possible future goalpost for ShakeAlert acceptance?
3m from 1m wide creek waterfall

## Slide 11
below this line is “nice to have” for ANSS purposes; not very relevant for ShakeAlert
>140m

## Slide 12
Noise floor and “small bumps” metrics look similar- very good stations aside from UO.WALD (13m from road).
UO.LAKE (34m from road) is “Not great, but probably squeaks by S.A. acceptance”
UW.WEL1 ”on” dam is bad (not plotted). UW.WEL2 200m away just off of dam is good
Only dams and power substations.

## Slide 13
Only stations labeled by tech with “known compressor or other loud thing nearby”
-Noise floor not affected very much by this.
-Most the the bumps are not big. But they are frequent.

## Slide 14
Using a station report to identify a problem.
HNE component clearly much higher noise floor than other components.
mm/s^2
A day’s worth of data with noise floors reaching 0.2 cm/s^2 which probably couldn’t see a M2 only 50km away.
1 day of data at UW.BAYC

## Slide 15
UW.BAYC coupled to building with a fridge on other side of wall?? = no Bueno.

## Slide 16
Directional & “big picture” photos help, please take them. No bueno:

## Slide 17
UW.LCMC Thank you for taking these photos that show station, tower, and generator with orientation and ability to gauge distances. Great remote station! Sensitive to very many triggers during windy times, but they are low amplitude.

## Slide 18
UW.HICC coordinates need to be updated (moved S by 4m)

## Slide 19
Limited school in session, excellent “indoor” station.
Metadata needs to be checked, 70m off.
Have undergrad verify IRIS/SIS coordinates w google maps and pnsndocs?

## Slide 20
Rivers: All the noise issues are only on E component  it’s only the white water that matters.
Note to coordinators: station review pages shows EPIC triggers are very low… this is because noise is mostly on E not Z component.
Rivers

## Slide 21
UW.BLDG: most issues are business hours  RIVER at 150m doesn’t affect station
Rivers

## Slide 22
UW.KELS pretty high noise floor, not diurnal… maybe from the big river 250m away or something industrial?
Rivers

## Slide 23
Distance to road
Ummm…. No.

## Slide 24
UW.CVSD School in session in Spokane. Not a great station, but useful.
Most significant noise is weekday only  likely foot traffic  92 m from road is far enough to hide car noise.
Distance to road

## Slide 25
HNE is quiet, so unlikely driveway noise  probably foot noise?
UW.EYES
Nearby road only 34m away.
Distance to road

## Slide 26
Only 28m to road, but 100m from stop sign
Distance to road

## Slide 27
Excellent example of consistently decent station at 74m to otherwise isolated road.
Distance to road

## Slide 28
Excellent example of not terrible very urban school, 24m to roundabout, 78m to road. (currently closed)
*Roundabout traffic is very slow, so road is likely biggest player
Pre-covid 75th percentile: 0.05 cm/s^2 noise floor, 6 EPIC triggers/hr, 0 spikes at 0.34 cm/s^2
Distance to road

## Slide 29
UW.LAYC: good example of an urban “good enough” station at 56m. Maybe try at St Martin U?
Distance to road

## Slide 30
UW.LARL 100m from road, but HVAC on other side of wall. 240 EPIC triggers/day.
Try to avoid…
HVAC

## Slide 31
I5 is at 170m is not a factor Feb 14ish = snow days, days beforehand had similar very high noise floor values  not an I5 effect.
UW.RBOK = portland
Towers & interstates

## Slide 32
Private homes can be good sites.
UW.LEVE, in a barn 67m to road, 85m to calm river, 14m to house.
Private homes

## Slide 33
Private homes can be good sites.
UW.MAC
-34m to road, but it’s just a dead end and a corner  low& slow traffic
-Road for nearby apt complex to NE is 44m but has a speed bump
-No busy road for along distance
-Parking lot to SE is 70m away
Private homes

## Slide 34
Private homes can be bad sites.
UW.MRN
-How busy is that road?
-Very diurnal pattern suggests its road traffic
Private homes

## Slide 35
Seattle Center- currently a pretty good station (100m to road), heavy foot traffic recently?

## Slide 36
Dams
108 vs 330m from falling water, off dam vs on fill (soft rock)
Not many spikes at either, but huge noise floor difference.

## Slide 37
FIN

## Slide 38
UW.BAYC
1mgal = 0.001 cm/s^2
HMSC plot shows 0.3 mg noise floor
Station plots never see hourly noise floor fall below ~0.02 cm/s^2 (20mg), typical is 0.15 cm/s^2 (150 mg)
Titan figure is from pnsndocs page, might have been wrong early configuration?
mm/s^2

## Slide 39
UW.LEWL

## Slide 40
Is this a recentering of the BB (Cascadia)?
Aluminum oxide settling.

## Slide 41
Very foot traffic heavy, but not awful. Different during non-covid times?

## Slide 42
Super quiet when school not in session.