## Slide 1: SSA 2022
Data Mining a Large Station Metrics Database to Guide Station Siting
Alex Hutko, Kyla Marczewski, Carl Ulberg

## Slide 2: SSA 2022
Introduction Conclusion
High-performance, cloud based database of metrics with alarms is really useful for a seismic network.
Roads are most noisy within 50m
Notes: Here’s my conclusion.

## Slide 3: SSA 2022 Seismic Quality Assurance Console GUI django backend API simple python read/write scripts
Notes: SQUAC is our Metrics database effort.
We’ve been working on it for over 3 years with lots of lessons learned.
Well documented wiki pages with examples

## Slide 4
What is SQUAC?
It’s a fancy metrics database & interface tuned for PNSN
Notes: Not too dissimilar from MUSTANG but tuned for PNSN as an ANSS RSN (often SMAs) and ShakeAlert partner.
There are many overlapping needs, but still some differences.
Now that we’ve done it, appreciate how much effort goes behind MUSTANG/DQA.

## Slide 5
What is SQUAC?
It’s a fancy metrics database & interface tuned for PNSN
Metrics: waveform- N big/small bumps, power, noise floor, peak Acc...
SOH- latency, gaps, completeness at datacenter
Variable granularity: 10 min/hourly/daily/monthly
Contributor source agnostic; currently 8 sources
Notes: Waveform based thing many are familiar with like power, but those don’t capture “bumps” well.
-16 full time CPUs @PNSN
-power from IRIS MUSTANG
-latency/gaps sniffed at 4 ShakeAlert centers on dev machines
-Caltech and Berkeley are contributing trigger counts for different algorithms

## Slide 6
What is SQUAC?
It’s a fancy metrics database & interface tuned for PNSN
Metrics: waveform- N big/small bumps, power, noise floor, peak Acc...
SOH- latency, gaps, completeness at datacenter
Variable granularity: 10 min/hourly/daily/monthly
Contributor source agnostic; currently 8 sources
AWS EC2 w RDS db, 2-10 servers (autoscaled), S3 archive ~$500/mo
~2 Billion measurements (400 GB)
9 Million measurements/day (>100/sec)
Performance: Create_or_overwrite ~80 measurements/sec
Read ~500 measurements/sec
Notes: We tried hosting the database on a local machine, and it was just terrible performance.
-16 full time CPUs @PNSN
We’ll soon be calculating in the cloud.

## Slide 7
Creating your channel group
Notes: Can plot raw measurements or any of a dozen statistics.

## Slide 8
Creating your dashboards
Notes: Can plot raw measurements or any of a dozen statistics.

## Slide 9
Table widget:
Single view of multiple metrics over a time window
Notes: “agg” is the count of metrics that are failing the user-defined thresholds.

## Slide 10
Timeline- think: SeisNetWatch with thresholds/color gradients
Notes: We’ll color gradients

## Slide 11
Notes: Timeseries for detailed view of raw values

## Slide 12
Notes: Map view that looks similar to MUSTANGular because Kyla is the dev who made both.

## Slide 13
Alarms
Notes: - measurement upload counts
Is it within a range of two numbers or outside of the range.
- raw measurements or stats of data
- Granularity of time windows can be minutes/hours/days

## Slide 14
Notes: This is what we just set up and if you want to add additional alarms

## Slide 16
Alarms
Notes: Here is an overview of what was just set up. You see:
Some are now out of alarm with the time stamp.
Some have never gone into alarm.
Some are in alarm and it shows the number of channels breaching the thresholds.

## Slide 17
Alarms
Notes: Email includes all the alarm information including newly breaching channels, as well all breaching channels.
Can also use as a monitor on metric uploads  tell you if a machine is down or out of memory

## Slide 18
Holistic views & Data mining
Notes: Shifting gears on use cases of the database.

## Slide 19
Use case: holistic report of station over past few weeks
Notes: Strong motion station at an elementary school.

## Slide 20
Use case: holistic report of station over past few weeks

## Slide 21
Updated 2x/week: https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS/
Use case: holistic report of station over past few weeks
Reports for most stations in ANSS:

## Slide 22
Updated 2x/week: https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS/
Use case: holistic report of station over past few weeks
Techs were informed something wrong w HNE. pier was coupled to house foundation :-(
Reports for most stations in ANSS:
Notes: https://seismo.ess.washington.edu/ahutko/STATION_METRIC_REPORTS/
Only PNSN & ShakeAlert stations are being sniffed for latency & gap info.
These Station Metric Reports have >40k measurements shown. Red dashed lines show the median value at the 95th percentile worst station in the PNSN for the shown metric aka typical values for a “bad” station. Colored numbers show % of time measurements exceed the red dashed line…. I.e. % of time it is really bad for that metric.

## Slide 23
How far away from a road should I go?
Distance to road (m)
Hourly count of small bumps (EPIC triggers)
0
10
20
30
40
50
40
60
20
80
100
120
0
Notes: This is about 100 PNSN strong motion stations
Colors and symbols are indoor/outdoor, fire station/school etc
Distance to road is the distance to not-slow traffic. Not speed bumps and roundabouts and stop signs.
75th percentile highest values are plotted which captures “what does it look like during business hours”

## Slide 24
Distance to road (m)
Hourly count of small bumps (EPIC triggers)
0
10
20
30
40
50
40
60
20
80
100
120
0
How far away from a road should I go?
50 m
Notes: 75th percentile highest values are plotted which captures “what does it look like during business hours”

## Slide 25
Distance to road (m)
0 20 40 60 80 100 120 140
cm/s^2
0.02
0
0.04
0.06
0.08
0.1
0.12
0.14
How far away from a road should I go?
Noise floor

## Slide 26
Distance to road (m)
0 20 40 60 80 100 120 140
cm/s^2
0.02
0
0.04
0.06
0.08
0.1
0.12
0.14
How far away from a road should I go?
Noise floor
50 m

## Slide 27
Road noise experiment
50 m

## Slide 28
Road noise experiment

## Slide 29: SSA 2022
Introduction Conclusion
High-performance, cloud based database of metrics with alarms is really useful for a seismic network.
Roads are most noisy within 50m
squac-help@uw.edu
Notes: Two part talk: database then data mining